MANUAL FOR WIRELESS PASSIVE INFRARED DETECTOR

PRODUCT INTRODUCTION

The product is wireless passive infrared detector with high stability. It has adopted advanced technology in signal processing and provided superhigh detection ability and anti e r r o r a l a r m . T h e d e t e c t o r w i l l d e t e c t m o v e m e n t o f h u m a n automatically when intruder pass through the detected area, a n d i t w i l l s e n d o u t a l a r m s i g n a l t o a l a r m h o s t i f t h e r e i s movement. The product is suitable for the safety of residential house, villas, factories, markets, warehouses, office building etc.

PRODUCT PROFILE

MAIN FEATURE

ASIC Adopted

Auto temperature compensation

Send alarm signal by RF

No wiring, install conveniently

Low battery indication

SMT design adopted

TECHNICAL SPECIFICATION

Operating voltage: 9V (powered by battery)

Static current: 25uA

Alarm current: 15mA

Detecting distance: 8m

Detecting angle: 110

Code form:1527

Radio frequency: 315MHz or 433MHz

Radio distance: 200m (open area)

Low battery indicator: blue LED

Alarm indicator: red LED

Sensor: dual element infrared sensor

Operating temperature: -10 to +50

Environment humidity:  95% RH (no congelation)

Anti RF interference: 10MHz	1GHz 20V/m

Installation mode: wall mounted or hanged in corner

Installation height: 1.7 to 2.5m (2.2m is Proposed)

Outline Size: 59L*45W*107H mm

INSTALLATION

- Installation at the out door,place with pets, air-condition n e a r b y, d i r e c t s u n s h i n e , h e a t s o u r c e a n d u n d e r t h e rotating objects should be avoided.

- Surface of installation should be firm with no vibration.

- Installing the detector in the place where intruder pass easily.

- Fixing bracket on the wall by screw.

- Hang the detector, it will work normally after turning on the power switch.

OPERATING INSTRUCTION

Product testing

1.Turning on power switch to ON, the LED indicator will be flashing 1 time. If you move front the motion sensor, the alarm LED indicator will be on 1 time,which means the sensor is triggered by movement

2. the interval time between 2 triggers is fixed 6 seconds, which means the sensor is only triggered again in 6 sec

NOTICE

- Please install and use the detector according to this manual, don't touch the surface of sensor for avoiding affecting the sensitivity of the detector. Please shut off power and then clean the sensor by soft cloth with little alcohol if cleaning needed.

- The product can reduce accident but may not perform as e x p e c t e d . T h e u s e r i s a d v i s e d t o t a k e a l l n e c e s s a r y precautions for his/her safety and the protection of his/her property.

- In order to ensure it can work normally, the power should be kept to supply and get on walking test periodically, once a week is better.

MANUAL FOR WIRELESS PASSIVE INFRARED DETECTOR

| Detecting Area View | Planform |
| --- | --- |

Side View