Wireless Easy Water leakage detector

User manual

DESCRIPTION

DIY. Application for detecting easy water leakage. Easy-to-used and operated. Widely for bathroom and any place where needs to protect water leakage .It is including one transmitter and one water sensor. The water sensor is installed in small case.

SPECIFICATION:

Transmitter index:

- Triggered by water from water sensor.

- Working voltage:12V DC, with dry battery model:23A . Low battery voltage about 8V.

3. Working current:≤10mA	Static current: ≤5μA

- IC EV1527 Oscillator resistor:330k (or others)

- Working frequency:433.92 MHZ or 315 MHZ

- Transmitting distance:noninterference<200m

7. Emitting frequency:<10mw	Frequency tolerance:±0.2MHz

- Operating temperature: indoor -10 ~ 50℃, related humidity ≤ 95%

- Power: standby :0.01W, Alarm :0.09W

- Size: Transmitter: 90 mm(L)×55 mm(W)×22 mm(H), small box size:  5x2.7x0.9cm,Net.weight:0.05kg

Water sensor index:

Material: fine copper, twin cable 2x1/0.4

Max switch power:10W

Working temperature:-40--+80℃(higher temperature optional)

INSTALLMENT

- Fixed code by IC1527;

- Fix the transmitter part higher than the water sensor rod, water sensor is mounted by screw or sticker paper the wall or place where need to protect water leakage.

- It means OK if the Signal LED flashes for 1 second after connecting with battery.

- The signal red LED flash for 1 second to alarm, the low battery green LED lights all along which means batter power is not enough. Please replace the same size new battery

- Antenna is suggested to pull out. （if 1527，ready to learn by main controller）