Wireless solar siren

I、Feature：

1、waterproof case；

2、Intelligent Control；

3、Built-in backup high-energy lithium batteries, solar charger；

4、 Tamper alarm;

II、Technical：

1, Power consumption: static: ≤16 m

Dynamic: ≤220 mA
2, Back-up battery: 3.7v 4400ma / h
3, The solar charging current: 180mA
4. Electricity charge: 110 ~ 240VAC, USB 5V, charge time: ≤12 hours
5, Continuous cloudy standby time: ≤10 days
6, the longest sound and light alarm time: 3 minutes.
7, receiving distance: ≥150 meters (open area)
8, alarm volume: ≥105db.

III.install and use
1. Open the battery switch or via USB power supply, siren "drip" sound, LED light flashes 5 Next extinguished into standby mode, will flash every 5 seconds;
2, the siren and wireless alarm host by studying the mating success of learning is connected with the operating instructions;
3. After studying the mating success off the power, and then select the appropriate location, by installing a hanging hole and then turned on permanently installed power supply;
4, wireless sound and light alarm after alarm is triggered the longest time is 3 minutes, or automatically stop when the radio alarm panel is disarmed.
   5, when the LED is no longer flashing about every five seconds, it means the battery voltage is low, shall be charged;
   6. Removing the power is wireless siren will immediately sound and light alarm;

IV, Operating instructions  connect the  wireless alarm host  
a, increase the allocation
1, turned Siren power, press the learning key, the alarm flashing lights;
2, emergency alarm button on the wireless alarm host by which to study mating, and then use the buttons on the control panel to disarm operation, when the radio sound
Alarm siren flashing light flashes five times off, the study mating success.
3, each wireless sound and light alarm can be connected with up to 2 wireless alarm host, each wireless alarm host can be connected with a plurality of wireless sound and light alarm;

b, deletion configuration
Energized state, often hold the Wireless siren learn button for 5 seconds and then release, warning lights will flash goes out, indicating that the deletion was successful.

Note:
1, to add or configure the operation, you can only operate configure a wireless siren;
2, increase the allocation operation, the control panel can only be operated by its own keys;
3, each wireless sound and light alarm can be connected with up to 10 wireless alarm host, each wireless alarm host can be connected with a plurality of wireless sound and light alarm;