English

Installation Instr uctions

W ireless Intelligent 2 PIRs Outdoor Motion Detector W ith Solar Power

1. INTRODUCTION

KI-40DP is a dual pir out door wireless detector with intelligent solar charging technology. This detector adopts intelligent multi-grade digital recognition technology and unique SLT calculation to process the 2-way special pir signal and 1 way environmental temperature signal to reach the topgallant detection and lowest false and missing alarm. It can recognize waving object and real human motion; resist direct or reflective sunshine and accommo-date the false alarm caused by speedy hot and cool air.

KI-40DP can operate in out door severe environment for long term. 8 bands of sensitivities for option, can take on the weather difference caused by rain, snow, hail, strong sunshine, gale etc, it is a purely high-class outdoor detector worthy of selection and usage.

  - BRIEFINTRODUCTION

- 2 Dual PYRO Sensors

- VLSI based electronics with movement speed spectrum analysis.

- 8 bands of sensitivities for option

- Anti direct or reflective sunshine

- Anti strongly mutative hot/cool air

- Pet immunity25KG

- Digital environmental temperature detection

- Intelligent solar charging technology

- Purely wireless transmitting structure, easy installation

- Tamper&low voltage alarm

- IP65 water proof, high-strength optical system

- Lens for option: long range, curtain, pet immunity

- Installation way: wall mount, corner mount, ceiling mount

- Transmission frequency for option 315MHZ 433MHZ - Mounting Bracket adjustment options: 90 ( h) and 30 ( v)

| 3. SPECIFICATIONS |  |  | +6m |
| --- | --- | --- | --- |
| Power supply: | 3*1.2V AAA Ni-MH Chargeable battery |  |
| Current: | Static ---200uA | Alarm ---15mA | 2m |
| Warm up period | 40s |  |  |  |
| Install high: | 1.5m.-2.4m |  |  |
| Alarm time: | 2s |  |  | 12m |
| Anti RFI/EMI: | 0.1-500MHz/3V/m |  |
| Anti-white light: | >100000LUX |  | SIDE VIEW |
| Low battery alarm: | 3.3V |  |  | -6m |
| Temp compensation: | intelligent digital compensation |  |
|  |  | TOP VIEW |
| Temperature: | -10 /+55 |  |  |  |
|  |  |  |  | Standard Lens |
| Humidity(RH): | 95% |  |  |  |
| Sensitivity: | 8 grades adjustable |  |
| Detect speed: | 0.2m/s to 3.5m/s |  |  |
| Radio emission | 200m | Open space |  |
| Frequency: | 315/433MHz etc. |  |  |
| Encoding: | PT2262 |  |  |  |
| Dimensions: | 160mm*65mm*50.5mm |  |
| Coverage: | 12m*12m | 110 | Standard Lens |  |
|  | 12m*3m | 12 | (Curtain Lens) |  |
|  | 12m*12m | 110 | (Pet Lens) |  |

Note the factory lens is standard lens, but we have 3 other lenses for option: pet immunity; curtain & long range!

| +1.5m | 2m |
| --- | --- |
| -1.5m | 12m |
| TOP VIEW | SIDE VIEW |

Curtain Lens

+6m

2m

12m

SIDE VIEW

-6m

| TOP VIEW | Pet Lens |
| --- | --- |

4. INSTALLATION GUIDE

Even though 40DP can accommodate outdoor severe environments, the following factors shall be avoided during install-ation in order to get the reasonable detection:

| No direct facing cold | Mount on a secure and | Incorrect Installation |
| --- | --- | --- |
| /hot source | stable base/object | (with pet immunitylens) |

Detector

Place without enough sunshine such as eave and umbrage etc

| Keep away from strong | Keep away from high | Don't install on the tree, | Avoid moving vehicles |
| --- | --- | --- | --- |
|  |  | wire fence etc |  |
| electrical interferences | pressure power |  |  |

5. WALL FASTENING

I n o r d e r t o g e t t h e b e s t d e t e c t i o n a n d s i g n a l c o v e r i n g s c a l e , t h e detector should be installed at 1.5-2.4 meters (height) and in a c o r r e c t d i r e c t i o n a s F i g u r e 1 . E n s u r e t h a t t h e r e a r e n o obstacles , trees w h i c h c o u l d o b s t r u c t t h e w i d e a n g l e d e t e - ctionview.

Release the screw and remove the front cover gently by hand. If too tight, use a screw driver to prize the opening slot between front cover and the base from the bottom side near to the screw

L o o s e n t h e f i x i n g s c r e w o n t h e P C B r e f e r t o f i g u r e 3 , b r e a k through the relevant blind holes according to spot requirement a n d i n s t a l l a t i o n w a y ( F o r e x a m p l e , b l i n d h o l e s f o r c o r n e r installation must be broken through during corner installation; and those for wall mount must be broken through during wall m o u n t i n g ) , a n d t h e n f a s t e n t h e s o l a r b r a c k e t o n t o t h e w a l l together, be attentive that the screws holes on bottom bracket and solar bracket shall be complies on same position, don't be dislocated or devious.

Top shell buckle A

Top shell buckle B

Bottom shell buckle A

| 2 | 1 |
| --- | --- |

Figure 2

Procedure for closing the cover:

F a c e t h e B s h e l l b u c k l e o f u p p e r c o v e r t o t h e s l o t o f l o w e r c o v e r, a n d f a c e A s h e l l b u c k l e o f u p p e r c o v e r w i t h A s h e l l buckle of lower cover. Press the upper cover down to close the detector.

Fasten the wall mount accessory bracket to a stable surface at the correct installation height. Insert and twist the connection accessory into the bracket section mounted on the wall. Fasten the bracket section to the PIR housing. ( Figure 4)

1

2

3

Figure 1

Procedure for opening the cover:

- Release the screw on the external cover

- Insert the blade screw driver into the opening slot, press it and wind it to the arrow direction, so that the external cover can be opened.

| Wall rivet | corner rivet |
| --- | --- |
|  | wiring hole |
| corner rivet | Wiring hole |
|  | Wiring |

Figure 3

Figure 4

installation figure for wall mount bracket

Red led

6. INSTALLATION OF SOLAR BATTERY CABLE

Refer to the figure, cross the solar battery cable from the cable-lead slot on backside of the detector bottom cover, and then go ac r o s s f r o m t h e c a b l e - l e a d h o l e o n b o t t o m ; c o n n e c t i t t o t h e r e l e v a n t e x t r e m i t i e s o n P C B ( P a y a t t e n t i o n t o t h e p o l a r i t i e s ) N o t e : m u s t l e a d t h e c a b l e a c c o r d i ng to the guide lines above, never cross the cable from to p o f d e t e c t o r b y h a n d , f o r i t m a y damage the air proof and cause false alarm or invalidation.

Warning  if want to charge the battery by DC through the solar battery input extremity, the voltage must be limited        within 0.8-2.0V, overload will damage the detector!

Do keep in mind!

7. PCB LAYOUT

For solar battery connection (care for the polarities)

DIP switch

LED PIR1

Vertical Adjust

Data set

Battery input

Oscillation

Resistor

Regulation

Address set               PIR2

External

Antenna	TAMPER

Transmission	RECODE

Module

Transmission

Antenna (315M or 433M)

Note: Don't touch the transmission module, transmission antenna or PIR on PCB.

8. SETTING

Dip switch setting

DIP 1 When dip switch 1 is OFF , detector is in high sensitivity mode; When dip switch 1 is ON , detector is in low sensitivity mode.

DIP2 when dip switch is OFF , detector is in normal operation mode , ie, i n o rd e r t o re a c h t h e p u r p o s e o f e n e rg y s a v i n g , in operation mode , when detector is triggered alarm, the 2 nd alarm shall be performed 3 minutes later.

When dip switch 2 is ON , detector is in TEST MODE , ie, detector c a n b e t r i g g e r e d w h e n a n y a l a r m s i g n a l a c c o r d w i t h a l a r m c o n d i t i o n s is detected.

This is for the convenience of installation and adjustment. DIP3 DIP4

DIP3 DIP4 is combined switch mode

It is for detection of different pulse setting. ts makeup is as below

| DIP3 | DIP4 | Pulse Mode |  | ON |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| OFF | OFF | 2 Pulse |  |  |  |  |  |  |  |  |  |  |  |
| OFF | ON | 3 Pulse |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | 1 | 2 | 3 | 4 | 5 |  |
| ON | OFF | 4 Pulse |  |  |  |  |  |  |  |
| ON | ON | 5 Pulse |  |  |  |  |  |  |  |  |  |  |  |

Suggestion: during operation in different environments, please adjust the detector to relevant setting in order to fulfill its best function.

DIP5 LED control

When it is  OFF LED is turn off to reach the purpose of energy saving and

concealed installation.

When it is  ON , LED is turn on.

Note: Strongly suggest that Dip switch 2 & 5 must be set to “OFF”, or battery life will be shortened greatly!

Encoding operation (communication with control panel)

4 0 s e c o n d s a f t e r p o w e r w a r m u p , s e t t h e c o n t r o l p a n e l t o "detector zone record mode" and then draw out the RECODE j u m p e r f r o m K I - 4 0 D P, a t t h i s t i m e , d e t e c t o r w i l l s e n d a n a l a r m s i g n a l t o c o n t r o l p a n e l , p l e a s e c o n f i r m t h e e n c o d e i s successful according to relevant operation on control panel

Note: jumper cap doesn't need to insert back after encode succeeds, if not, tamper function will disapear.

RECODE

Installation of chargeable battery

| 1. Switch DIP5 to “O N” position. |  |  |  |  |
| --- | --- | --- | --- | --- |
| 2. O p e n t h e metal c a p o n b a t t e r y b o x , |  |  |  |  |
| c o n n e c t t h e 3 * A A A battery group |  |  |  |  |
| ( f o r o p t i o n ) t o t h e m o t h e r b a s e o n |  |  |  | Battery |
| A f t e r b a t t e r y c o n n e c t i o n , L E D |  |  |  |  |
| detector and take care of its polarities. |  |  |  |  |
| doesn't flash, states that the polarity |  |  |  | input |
| is wrong or battery is bad. |  |  |  |  |
| D r a w i t o u t a n d m a k e a c o n v e r s e |  |  |  |  |
| c o n n e c t i o n , i f L E D d o e s n ' t l i g h t , |  |  |  |  |
| must make a careful check and solve |  |  |  |  |
| the problem beforethe 3 rd connection. |  |  |  |  |

Walk test

Preparation:

after power connection, set DIP2 & DIP5 to “O N” position.

- Set different pulse modes refer to different environments. Detector is with 8 kinds of operation modes as below:

|  | DIP1 |  | DIP3 | DIP4 | Mode | Relevant environment |
| --- | --- | --- | --- | --- | --- | --- |
|  | OFF |  | OFF | OFF | High sensitivity &2 Pulse | Very High Risk |
|  | OFF |  | OFF | ON | High sensitivity &3 Pulse | High Risk |
|  | OFF |  | ON | OFF | High sensitivity &4 Pulse | Risk |
|  | OFF |  | ON | ON | High sensitivity &5 Pulse | Low Risk |
|  | ON |  | OFF | OFF | Low sensitivity &2 Pulse | Risk |
|  | ON |  | OFF | ON | Low sensitivity &3 Pulse | Low Risk |
|  | ON |  | ON | OFF | Low sensitivity &4 Pulse | Noisy Area |
|  | ON |  | ON | ON | Low sensitivity &5 Pulse | Extreme Noisy Area |

2. Close the front cap, when LED indication is off, perform a transverse movement to check the PIR performance through the red LED, this can avoid

the dead angle of PIR detection. PIR is in

highest sensitivity when movement is transverse to the

detector.

Rev .02 12/19

Setting of compliance with other control panels

Oscillation resistor set:

Compliance with other c o n t r o l p a n e l s c a n b e r e a ched through regulation of oscillation resistance on encoding chips. Refer to below figure, our oscillation resistance is with 3 modes: 4.7M, 3.3M, 1.5M

Data set:

C a n b e s e t b y t h e j u m p e r s a s f i g u r e " D ATA S E T " , a m o n g w h i c h 1 = D 3 ( A 8 ) ; 2 = D 2 ( A 9 ) ; 3 = D 1 ( A 1 0 ) ; 4 = D 0 ( A 11 ) , p l e a s e s e t i t correlatively according to the requirement of control panel

Address set:

Can by set by the jumpers as figure "ADDRESS SET" in order that control panel can distinguish different zones

External transmission antenna

U s e r c a n e n l a r g e t h e w i r e l e s s t r a n s m i s s i o n d i s t a n c e b y c o n n e c t i n g a n e x t e r n a l a n t e n n a a s t o t h e b e l o w f i g u r e .

Note:

1.the resistance of external antenna must be 50 Ohm and 1/4 wavelength from 315M or 433M.

2.Normally we don’t suggest external antenna, when transmission distance can’t satisfy the needs, please do remove the internal antenna and then connect the external one.

| 1 | 2 | 3 | 4 |
| --- | --- | --- | --- |
| Data set |  |  | L |
|  |  |  | H |
| Oscillation 4.7M |  |  | External |
| Resistor | 3.3M | Antenna |
| Regulation |  |  | 1.5M |
|  |  |  | (Either connector is ok) |
| Address set |  |  |  |

9. VERTICAL ADJUST

2.1 3.1	5.9	15

-1

1	2.1m

+1

4m

|  | 3.9 | 6 | 10.4 | 15 |
| --- | --- | --- | --- | --- |
| 1.8 2.7 | 4.8 | 13 |  |
| -1 |  |  |  |  | 2.1m |
| 1 |  |  |  |  |  |
| +1 |  |  |  |  |  |
|  |  |  |  |  | 4m |
|  | 3.4 | 5.2 | 8.7 | 15 |
| 1.5 | 2.3 | 3.7 | 8 |  |

| -1 |  |  | 2.1m |
| --- | --- | --- | --- |
| 1 |  |  |  |
| +1 |  |  |  |
|  |  |  | 4m |
| 2.9 | 4.4 | 7 | 15 |

10. NOTES AND WARNINGS

Even the most sophisticated detectors can sometimes be defeated or may fail to activate due to: DC power failure/improper connection, malicious masking of the lens, tampering with the optical system, decreased sensitivity in ambient temperatures near that of the human body and unexpected failure of a component or circuit. The above list includes the most common reasons for failure and it is recommended that the detector and the entire alarm system be checked weekly to ensure proper performance.

An alarm system should not be regarded as a substitute for insurance. Home & property owners or renters should be prudent enough to continue insuring their lives & property even though they are protected by an alarm system.

WARNING! Changes or modifications to this unit not expressly approved by the party responsible for compliance could void the warranty. This device has been tested and found to comply with the limits for a Class B digital device, pursuant harmful interference in residential installations. This equipment generates and uses or radiates radio frequency energy and if not installed and used in accordance with the instructions, may cause harmful interference to radio and television reception. There is no guarantee that interference will not occur in a particular installation. If this device does cause such interference, which can be verified by turning the device off and on, the user is encouraged to eliminate the interference by one or more of the following measures:

- Increase the distance between the detector and the electrical/electronic equipment.

- Connect the device to a different power socket which supplies power to the detector.

- Consult the dealer or an experienced radio/TV technician