Wireless LCD keypad user guide

Function

1) Calendar function

2) It works with the alarm system, and can carry on the function of arm/disarm/emergency by password

3) It can receive the wireless signal from alarm system to show the status and prompt

4) One button programming, password recovery

Technical parameter

1) Power: DC12V

2) Power consumption: <50MA

3) Transmit: encoding chipset: single chip simulates ev1527, chipset code: 433 MHz, Timing resistor: 330K

4) Receive: Decoding chipset: single chip learning style; frequency: 868 MHz Timing resistor: 330K

Working principle

It works with the alarm system, generally installs in the entrance, operates the keypad with password to control alarm system arming and disarming; and show the state of alarm system arming/disarming at real time. If we arming/disarming alarm system by the remote controller or the button of alarm system directly, the system will send the wireless signal to wireless keypad to show its synchronic state, if the system make alarm, the keypad will show the system is in alarm state, if the system disarmed, the keypads will also disarming.

Operating

1) Program menu setting: Press SET-(4 passwords)-ENT to the following menu setting:

Time setting: Press ENT,then put 6 numbers,2 for” hour” 2 for”minite 2 for “second”

Date setting: Press ENT, then put 7 numbers, 2 for “year” 2 for “month” 2 for “date” 1 for “week”, number 0 express Sunday

Wireless study: Press ENT, to chose study/clean study or clean the transmit signal.

Transmit address code set: Press ENT then put 8 numbers (A0-A7),for example “22110022”, 2 express low level, 1 express high level, and 0 express vacant code, after setting, press ESC out.

Change password

1) User password: this password used for arming and disarming the system.

How to change?

SET-9999-ENT-choose change the user password -ENT- put old 4 program password (8888) -ENT- put new password -ENT- put new password again-ENT, exit automatically.

2) Program password: this password used for setting time, date and wireless address code etc.

How to change?

SET-9999-ENT-choose change the program password-ENT-put old 4 password-ENT-put new password (8888)-ENT-put new password again-ENT, exit automatically.

Mark: If the users forget the program password, please press the button on back for 5 seconds,”BI.”Sound for a while, the program password will return to 8888

Arming/disarming and emergency operating

1) Arming away: Press arm button-User Password (111111)-ENT-choose arming away-ENT, when you hear “di” sound from wireless keypad and alarm system, arming successfully.

2) Arming at home: Press arm button-User Password (111111)-ENT-choose arming at home-ENT, when you hear “di” sound from wireless keypad and alarm system, arming successfully.

3) Disarming: Press disarming button-User Password (111111)-ENT-“di di” sound from wireless keypad and alarm system, disarming successfully.

4) Emergency operating: press emergency button to send emergency alarm signal to alarm system.

Study operating

A. Study the keypad to system: set the system to study state (detailed settings please refer to the manual of system), arming or disarming the keypad for 2 times. The system indicates that study successfully.

B. Study the system to keypad: set the menu of keypad to study state, arming or disarming the system for 2 times. The keypad indicates that study successfully.

LED board indicator light guide

1) At home: Arming at home, the light on.

2) Power/battery: 8s flash one time, if the battery is low, the light N.O.

3) Arming: arming at home/arming away, the light on.

# Text boxes

At home                   power/battery            arming

〇                  〇                  〇